## Slide 1: Tompkins Robotics Team 5427
Safety Presentation

## Slide 2: Tompkins Robotics Team 5427
BASIC SAFETY TRAINING
5427 Basic Safety Training Rev. A

## Slide 3: Steel Talons Safety Principles
YOU are responsible for keeping the Steel Talons team safe
ANYONE can STOP ANYONE doing ANYTHING that is UNSAFE!
  Anyone not wearing proper PPE – STOP THEM
  Anyone using any tool in an unsafe manner – STOP THEM
  Anyone who is acting unsafely – STOP THEM
  If YOU see an unsafe situation – FIX THE SITUATION

## Slide 4: RSC Safety Building Emergency & Equipment
Solenoid Valve
A = Emergency Exits
B = Extinguishers
C = Fire Alarm Pull
D = AED
E = Safety Shower / Eyewash
F = First Aid Kit
G = Goggle Sanitizer
A
A
A
A
B
B
B
B
B
B
B
B
B
B
B
C
C
C
C
D
E
F
F
F
F
F
F
F
F
F
G
G
G
G
G
G
G
G

## Slide 5: Steel Talons & RSC Safety Rules
  Adult Supervision
  KISD employee must be present in building
  Two mentors required on site, one may be the KISD employee
  No one-on-one student/adult work
  No unsupervised student work
  Building secured by KISD employee after work session
Sign in and out at the front door to our bay
RSC requires students to swipe their badges when entering building and the bay
Parents are expected to pick up students promptly after sessions
Be courteous to our neighbors in the RSC
No open flames in the building
Solenoid Valve

## Slide 6: Steel Talons & RSC Safety Rules (continued)
  Safety glasses
  Required in work bays, central shop, and within 5 feet of field when in use
  Must meet OSHA Z-87
  Side shields required (or compliant wrap-around glasses or goggles)
  Normal glasses with side shields do NOT satisfy this requirement
  Glasses must be clear or only lightly tinted – we must easily see your eyes
Shoe requirements
    Substantial, closed-toed shoes shall be worn in all work areas
    Required within 5 feet of the central field area of the RSC
    Flip-flops, sandals, flats, “Crocs”, and other footwear that has open holes are not permitted
    Sole of shoe must resist puncture
Other personal protective equipment (PPE)
    Specific PPE required in areas defined by KISD and building administration
    Our team has specific PPE for each tool posted near each tool station
    Wear appropriate gloves when handling sharp materials (leather or cloth) or handling chemicals (rubber or plastic) – we have more hand injuries than anything else
    Use ear protection as needed – see the tool station requirements
Solenoid Valve

## Slide 7: Steel Talons & RSC Safety Rules (continued)
  Loose Clothing, Jewelry, Hair, Hoodies, etc.
  Shall be kept out of the way when working with power tools
  Do not wear rings when working with materials
  Do not wear long-sleeves or gloves when working with potentially entangling tools (e.g. mill, drill press, belt sander)
  Tie back long hair; remove jewelry; roll up long sleeves; take off hoodies
Training Requirements
    Proper training in safe use required to operate a power tool. Includes everyone working at the RSC (mentors and students)
    Each team has people trained to teach others on their team the required procedures
    We maintain records to demonstrate this requirement has been met
Team Safety Programs
    Within our bay, we have more strict safety requirements than the RSC
    Use proper tools, in good condition, for each job
Contact mentors immediately if any problems arise or if you don’t know how to do something
Solenoid Valve

## Slide 8: Steel Talons & RSC Safety Rules (continued)
  Chemicals & Paint Usage
  No use of volatile or vapor emitting chemicals in the building
  No spray painting in the building – OK out back with adult supervision
  Proper PPE required when handling chemicals – e.g. gloves
  Materials must be used in accordance with the manufacturers instructions
  We have MSDSs (or SDSs) available for the chemicals we use in our area
  In the event of a spill, notify KISD representative and mentor
  Behavior
  No horseplay or rowdy behavior on the premises
  Food and Drinks
  No food or drinks (except water) in the bays
  Food is allowed around the central bay (not on the carpet) and outside the building (patios)
  Wash hands thoroughly with soap and water before handling food or drink
Solenoid Valve

## Slide 9: Steel Talons & RSC Safety Rules (continued)
  Daily Housekeeping Requirements
  Keep areas clean and uncluttered
  Keep emergency exits clear
  Keep carpeted area clear of debris and cuttings, no drilling or cutting on carpet
  Clean up begins 15 minutes before the end of a session
  Clean area before you leave
  Trash and recyclables are to be cleaned up and disposed of in the proper locations
  Floor shall be swept and vacuumed as needed
  Tools, surplus raw materials, and other items shall be put away when finished with them
  Clean up the area outside if it has been used for painting or other activities
  All power should be turned off at the end of the day
Solenoid Valve

## Slide 10: Steel Talons & RSC Safety Rules (continued)
  Incident Reporting Requirements
  Report any incident resulting in injury, fire, or damage to people, building, or equipment immediately to a KISD representative and a mentor. This includes minor first aid incidents such as a band aid
  Report near-misses which could have resulted in injury to our safety team
  To report an injury or near-miss to our team, use the form at the sign-in table
  To report an injury to the RSC, go to the RSC administrator’s office
Solenoid Valve

## Slide 11: Why Safety?
What are your answers to this question?
Here are some from Team 5427
  Your parents want you to take care of them when they get older!
  It is always fun until someone loses an eye!
  We are Tompkins Robotics, not Tompkins Do Crazy Stuff Until Someone Gets Hurt!

## Slide 12: Safety Ground Rules
Safety is YOUR job. Never assume someone else is doing something safely!
See something unsafe? Tell people. If you see ANYONE doing something unsafe STOP THEM!
Cleanliness and Organization are foundational keys to safety.

## Slide 13: Safety Ground Rules
Plan your work before you do your work
Discuss what you will be doing with your team mates.
What are the risks that you may encounter? How can you mitigate those risks? Planning your work allows you to prepare to stay safe.

## Slide 14: Protecting Yourself
Be aware of EVERYTHING around you.
Always wear your PPE.
  Personal
  Protective
  Equipment
    PPE is a fashion statement. It states that you want to stay fashionably alive and unhurt!

## Slide 15: PPE Eye Protection
Safety Glasses – Protecting Your Eyes
  Must be worn at all times in all areas around the robot.
  Must be ANSI approved. Look on the side of the glasses for the ANSI z87 mark.
  Must have side shields, or wrap around protection.
  Must be worn over prescription glasses, if your glasses do not have side shields or are not ANSI approved.
  Splash goggles or a face shield must be worn OVER safety glasses if handling liquid chemicals.

## Slide 16: PPE Eye Protection

## Slide 17: PPE Hearing Protection
Safe hearing range is 70 dB over
8 hrs.
Every 3dB increase doubles the
sound energy or impact
A whisper, 30 dB, is 1,000 times
louder than the softest sound you
can hear.

## Slide 18: PPE Hearing Protection
Hearing loss is permanent
Can occur gradually over time, due to acute and chronic noise.
Proper protective equipment
  Ear Plugs – FOLLOW DIRECTIONS ON USE
  Ear Muffs
Must be worn when power tools are in use or if Rolling Stones are performing a concert in the work area.

## Slide 19: PPE Hearing Protection
ACCEPTABLE
These are for work!
UNACCEPTABLE
These are for snuggling up when
it’s cold outside!

## Slide 20: PPE Foot Protection
NO
  Bare Feet
  Open toed shoes
  Sandals
  Flip Flops
  Bunny slippers
  Slippers
Shoes should be sturdy
Steel toed shoes may be required when lifting the robot or other heavy objects.

## Slide 21: PPE Hand Protection
Safety Gloves should be worn when:
  When cutting or working with sharp objects
  Working with soldering gun
  Handling metal and wood
  Lifting
  Chemically resistant gloves must be worn when handling liquids or leaking batteries
  Hanging around – just in case
  DO NOT WEAR GLOVES WHEN OPERSSTING ROTATING EQUIPMENT – THAT IS A SNAG HAZARD

## Slide 22: PPE Hand Protection
Safety Gloves prevent:
  Cuts
  Splinters
  Pinches – other than the ones from your relatives
  Scrapes
  Burns
  Chemical Burns
  Nail polish damage

## Slide 23: PPE - General
Long pants are recommended to prevent scrapes and cuts.
No loose clothes or neck ties. These can get caught in equipment.
Long hair is to be pulled back.
No long or dangling jewelry.
No Philadelphia Eagles clothing.

## Slide 24: Power Tools
Power Tools are great work savers:
  They reduce strain and effort
  Help reduce the time needed to perform a task
  Are easy to learn and operate
  Can allow work that might not be done without them.
  Give more precision than most hand tools
THEY WILL HURT, MAIM, OR KILL YOU!!

## Slide 25: Power Tools
Do not use power tools unless you have been trained and authorized
Treat them as if they were energized, always
Inspect each tool before using. You are responsible for your own tool inspections
Turn off and unplug or remove battery when not in use
“Test Fire” after turning off to de-energize
Never remove guards – ever
Alert those around you that you are using a power tool
Treat each tool with care

## Slide 26: Power Tools
Always return to their proper place when done.
Always secure your work piece
  Clamp it
  Bolt it
  Insure that it cannot move
USE PROPER PPE FOR EACH PIECE OF EQUIPMENT.

## Slide 27: Power Tools - Cutting
TABLE SAW
CIRCULAR SAW
SAWZ ALL
MITER SAW
BAND SAW
JIG SAW

## Slide 28: Power ToOls - Cutting
Injury Risks
  Cutting
  Flying debris / Inhaled debris
  Entangling and cutting
  Kick back or throwing a work piece.
Always assume it is energized!
Never touch the blade unless the saw is turned off, unplugged, and you have “test fired” the saw

## Slide 29: Power Tools - Drilling
Drill Press
Drill Sergeant
Dremel Drill
Power Drill

## Slide 30: Power Tools - Drilling
Injury Risks
  Cutting – the sides are sharp
  Debris
  Entangling on loose fitting clothes
  Work piece kick back or twirling
  Drill bit breaking and flying

## Slide 31: Power Tools - Abrasives
BELT SANDER
ORBITAL SANDER
BELT SANDER
GRINDING OR CUT OFF WHEEL

## Slide 32: Power Tools - Abrasives
Injury Risks
  Scrapes
  Debris – Inhaled Dust – Dust Mask Mandatory.
  Entanglement
  Grinding wheels and cut off wheels
    The name “cut off” says it all. It can cut pieces of you off!

## Slide 33: General Risks
Soldering – Burns
Work Area – Slip, trip, and falls.
  Clean up
  No horse play
  These are tools not toys
Hand tools
  Cuts
  Scrapes
  Pinches
  Whacks

## Slide 34: Take the test!!

## Slide 35: Be Safe!
And we’ll have a lot of fun!