## Slide 1: Resistance

## Slide 2: Definition
Opposition to the flow of electrons
When electrons pass through materials with high resistance, they collide with its molecules more often and in doing so transfer some of their energy into heat
Examples:
heating coils
light bulb filaments
fuses – metal that will heat up and melt and break if too much current passes through it

## Slide 3: Relationships
Resistance is measured by comparing the potential difference with the current
Plot of V vs I, V = slope(I) , slope = V/I

## Slide 4: Ohm’s Law
For any given conductor, the V/I ratio is constant
Ohms law – the potential difference between any two points in a conductor varies directly with the current between them
The constant slope is call the resistance ( R)
R = V/I
Units V/amp = 1 ohm (Ω)
Some non-metals are conductors that don’t obey ohm’s law (called non-ohmic)

## Slide 5: Examples
Find the resistance of an electric light if there is a current of .80A and the potential drops 120V as it goes through the bulb.
What is the potential difference across a toaster which has a resistance of 13.7 Ω when the current is 8.75A?
What is the current through a heater with a resistance of 38 Ω and a potential difference of 240V across it?

## Slide 6
A small flashlight bulb draws 300mA from a 1.5V battery. A) what is the bulb’s resistance? B) if the voltage drops to 1.2V, how would the current change?

## Slide 7: Resistors
Devices used to control the amount of current in a circuit
Symbol of resistor on diagrams
Two types
  Wire round resistors – coil of thin wire
  Composition resistors – made of some material that offers resistance (semi-conductor)
Resistors are rated by color code banding