POCATELLO/CHUBBUCK

SCHOOL DISTRICT NO. 25

Bannock County, Idaho

April 1, 2020

### Addendum No.2

RE:		ASPHALT MAINTENANCE AT VARIOUS DISTRICT SITES

School District No. 25

Pocatello, Idaho 83201

FROM:	Renae Bentley

Business Services

3115 Poleline Road

Pocatello, Idaho  83201

(208) 235-3220

bentlere@sd25.us

This Addendum becomes a part of the Contract Documents and modifies the original Bidding Specifications, as noted below.  Please make the following changes to the Asphalt Maintenance Bid Specifications.

PROJECT No. 1 – FRANKLIN MIDDLE SCHOOL, 221 E. Terry

DESCRIPTION OF WORK:  Basketball Court Asphalt Seal Coating (Area of construction to be determined at walk-thru and as indicated on attached plans)

CHANGE SCOPE OF WORK:  NEW asphalt pad.

Contractor shall remove all topsoil, debris and rocks from the areas to be paved and treat with a soil sterilant to inhibit future flora growth.  The subgrade should be properly shaped to meet true alignment and elevation.  Surface to be compacted to not less than 95 percent of maximum density.

Install non-woven fabric between soil and aggregate base.

Aggregate crushed base construction of six inches (6” of 3/4 minus) must be spread and compacted to the required six inches (6”), with two and one-half inches (2-1/2”) of surface hot mix.

BIDS FOR 2020 ASPHALT MAINTENANCE AT VARIOUS DISTRICT SITES TO BE OPENED ON APRIL 14, 2020 AT 9:00 AM”

Acknowledge receipt of this Addendum on the original Bid Form., failure to do so may subject the Bidder to disqualification

No other changes are made to the original bidding specifications:

NO OTHER CHANGES

END OF ADDENDUM No.2 – 4/1/20 rlb